Fuel Pressure Regulator:

I used a couple of ¼” cable clamps to secure the FPR bracket to the vacuum pipe going across the upper intake manifold.  I also ran a bolt through the center, inline with the existing hole on the black bracket attached to the manifold.  For bolts, I used some I had laying around with stainless lock nuts with the plastic inside.  Once installed, you may have to bend the assembly a little to make the FPR horizontal.  It came out a little tilted to the passenger side about a ½ inch.  The return line gets hose clamped to the stock return hard line.  Since the stainless steel braid tends to unravel after cutting, I put some ¾ inch heat shrink on the end.  Since I had a lot of heat shrink, I covered the whole line just to see what it would look like.  This could be an option in place of wire loom, but may make it more difficult bending the line in tight turns.  Looks nice though.